A device to control the high-voltage AC waveform, a processor to read temperature input and determine appropriate power output, a thermocouple and amplifier to measure temperature, and of course, the toaster oven. This tutorial only covers the high-voltage AC controller which consists of a TRIAC with over-current and over-voltage protection, an optoisolated TRIAC driver, and a zero-crossing detector. This device is designed to be microcontroller agnostic and while my component selection is catered to a 3.3V device, it can easily be adapted to 5V without much trouble.

A very common way of implementing an AC controller is with a solid-state relay. These allow the oven to be full ON or full OFF and the signal can be pulsed to get an approximate temperature (known colloquially as BANG-BANG controlling). A huge swath of the world's control systems run just fine this but it is neither elegant nor interesting to implement (in my opinion). Inside most solid state relays, however is a device called a TRIAC which can be ordered as a standalone device. Like Robert mentions in his article, it's essentially a bidirectional extension of the thyristor, or can be though of as a solid-state switch that conducts current in both directions.